## Slide 1
Research Progress and Prospects of Intelligent Design Methods for Ship Hull Forms
Wuhan University of Technology
Presenter: Feng Baiwei
October 2026
Ship Performance Multidisciplinary
Design Optimization Team

## Slide 2
Outline
1
Research Background
2
SBDO-Based Hull Form Optimization
3
GeneHull Intelligent Design Platform
4
AI Agents for Autonomous Hull Design
5
Summary and Outlook

## Slide 3
Energy saving and emission reduction have become a focus across industries. To meet national decarbonization goals, green shipping must be developed; ship design and construction must comply with IMO's EEDI and SEEMP requirements, and energy-efficient "green ships" have become the mainstream of modern ship design.
Energy saving
Research Background
Energy Saving Trend
Hull form design is one of the most important parts in developing green ships. The simulation-based design optimization method (Simulation Based Design Optimization, SBDO) has become the primary means of hull form design.
Means of Green Ship Development

## Slide 4
Research Background
Hull form determines ship resistance, propulsion, seakeeping and maneuverability — key hydrodynamic performance factors. Hull form design is a core part of general ship design and directly determines a ship's energy efficiency and operating economy.
Traditional hull design relies heavily on empirical formulas, systematic model-series charts and manual iteration by experts:
① Long design cycle and low efficiency;
② Design quality depends on personal experience; knowledge is hard to pass on;
③ Difficult to systematically search the design space for optima.
Hull lines plan (body plan): the traditional expression of hull design
Hull Form: Importance & Limitations
Importance of Hull Form
Limits of Traditional Methods

## Slide 5
Research Background
Traditional Empirical Design
Simulation-Based Design Optimization
Knowledge-Driven Intelligent Design
Autonomous Intelligent Design
CAD-assisted drafting with empirical formulas, lines charts and manual iteration; long cycles and little knowledge reuse.
CAD parametric modeling + CFD evaluation + automatic optimization (SBDO), moving from the "forward problem" to the "inverse problem" with performance-driven design.
Knowledge engineering and intelligent reasoning distill design knowledge into knowledge bases and rule bases; the GeneHull platform enables knowledge reuse and rapid design.
LLM-centered AI Agents understand requirements, plan tasks, call design tools and iterate autonomously — toward autonomous hull design.
Main thread: Deep integration of CAD × CFD × AI continuously raises design automation and intelligence
Evolution of Hull Design Methods

## Slide 6
Outline
1
Research Background
2
SBDO-Based Hull Form Optimization
3
GeneHull Intelligent Design Platform
4
AI Agents for Autonomous Hull Design
5
Summary and Outlook

## Slide 7
SBDO-Based Hull Form Design
Advance hull design from the traditional empirical mode toward a knowledge-based mode founded on advanced numerical evaluation;
Go beyond one-off CFD-based selection by systematically integrating CFD into the design optimization process, accelerating engineering application of CFD;
From the "forward problem" to the "inverse problem", achieve performance-driven design, raising the level of innovative hull design and the international competitiveness of China's shipbuilding industry.
Intelligent
Optimization Algorithm
Data transfer
Objective
Design Variables
Constraints
Intelligent CAD
Performance Evaluation
SBDO-Based Hull Form Optimization

## Slide 8
Developed a ship hull surface deformation module based on RBF
SBDO-Based Hull Form Optimization
Intelligent CAD
Solving the above equations yields all coefficients λi and ci, which can then be used with the original hull mesh points to determine the new mesh points.
Solution process
Φ is a radial basis function
p(x) is a low-order polynomial

## Slide 9
Example of smooth deformation of the hull surface
Forward deformation constrained by station positioning:
Constraint on the bow deformation of the waterline:
SBDO-Based Hull Form Optimization
Intelligent CAD
Variable point
Fixed point
Variable point
Fixed point
Initial
Deformation
Initial
Deformation

## Slide 10
Developed a ship hull surface deformation module based on FFD
Initial Bow Nose Point Cloud
Deformed Bow Nose Point Cloud
Comparison Of Spatial Point Clouds Before And After Deformation
Effect Comparison
Longitudinal Section Line Comparison
Transverse Section Line Comparison
Comparison Of The Hull Form Lines Of The KCS Vessel Before And After The Deformation Of The Bulbous Bow
SBDO-Based Hull Form Optimization
Intelligent CAD

## Slide 11
Propose a construction method for a uniform design scheme for large sample point numbers based on genetic algorithms
SBDO-Based Hull Form Optimization
Performance Evaluation
Dynamic selection of sample points
Selection of static sample points
Method for selecting sample points
Uniform Design Method
Static Sample Point Selection Method
Dynamic Sample Point Selection Method
Application Example
Disadvantages
The traditional selection method does not take into account the differences in the performance space.
Improvement
Proposed a dynamic selection method for sample points based on the principle of correlation.

## Slide 12
Research on the Construction of a Graph Neural Network Resistance Prediction Model Based on Ship Body Point Cloud
SBDO-Based Hull Form Optimization
Performance Evaluation
Address the issue of the generalizability of the proxy model. Currently, the construction of the proxy model involves users building approximate models for different optimization problems (with different optimization variables/parameters), which makes it difficult to achieve generalizability and insufficient in terms of generalization ability.
船体模型图
离散点云图
采样后点云图
Ship Hull Model
Discrete Point Cloud
Sampling Point Cloud
Schematic diagram of the PB-GraphPR network structure

## Slide 13
Deep learning prediction of ship wave depth
SBDO-Based Hull Form Optimization
Performance Evaluation
The constructed deep learning model can predict the height of free surface waves. It comprehensively represents the physical characteristics (dispersive waves, transverse waves) of the Wigley ship in still water with a current, and is basically consistent with the CFD results.
Conclusion
Construction of the loss function:

## Slide 14
Deep learning prediction of the three-dimensional flow field of the ship body
SBDO-Based Hull Form Optimization
Performance Evaluation
The proposed deep learning model can be used to learn high-dimensional physical quantities (velocity field, pressure field), and has the ability to fit complex high-dimensional nonlinear data. It provides an efficient and reliable offline model for subsequent ship shape optimization based on flow field information.
Conclusion
Q

## Slide 15
Improvement of multi-objective optimization algorithm based on physical planning
SBDO-Based Hull Form Optimization
Intelligent Optimization Algorithm
Multi-objective optimization algorithm
Improvement of multi-objective optimization algorithm based on physical planning
Improving the search position of the pseudo-preference structure in the target space
Rotating the pseudo-preference structure
Improved multi-objective optimization algorithm based on physical planning
Disadvantages
It is impossible to generate any arbitrary number of Pareto solutions; the distribution of search positions for the pseudo-preference structure is uneven; the search range of the pseudo-preference structure is limited.
Improvement
Employ the uniform experimental design method to uniformly distribute the pseudo-preference structure.
Utilize the rotation of the pseudo-preference structure and the reduction of the search domain techniques to obtain a uniformly distributed Pareto front.

## Slide 16
Propose a dynamic spatial reduction method based on data mining
SBDO-Based Hull Form Optimization
Intelligent Optimization Algorithm
Space reduction method
Extraction of optimized design rules
Dynamic Space Reduction Technology
Dynamic Dimension Reduction Technology
Dimensional variation and space optimization techniques
Disadvantages
Current domestic and international research has overlooked the implicit design knowledge contained in the simulation data.
The optimization process requires a large amount of sampling, which consequently limits the improvement of optimization efficiency.
Currently, all research is conducted in a single manner, either by reducing the spatial size or the dimension.
Improvement
Applying partial correlation analysis and self-organizing mapping technology to data mining for ship type optimization
Proposing a dynamic spatial reduction based on partial correlation analysis
Introducing an efficient dynamic variable space and variable dimension optimization framework

## Slide 17
(1)Ship hull surface discretization module
(2) Ship hull surface parametric module
(3) Ship resistance, maneuvering, and wave resistance interface module
(4) Knowledge acquisition module
(5) Optimization algorithm module
(6) Experimental design module
(7) Three-dimensional Visualization Module
(8) Post-processing Module
(9) Optimization Process Monitoring Module
(10) IGES Import/Export Module
(11) Hydrostatics Calculation Module
(12) Advanced Parameter Configuration Module
(13) Database Module
(14) Sensitivity Analysis Module
(15) Complete Stability and Salvage Stability Calculation Module
(16) Uncertainty Analysis Module
(17) Resistance Calculation Module
(18) Control Calculation Module
(19) Wave Resistance Calculation Module
(20) Approximate Model Module
Software for fine optimization of ship hull lines based on SBDO
SBDO-Based Hull Form Optimization
Analysis Tool Layer
User Layer
Ship hull surface deformation module
Ship hydrodynamic performance solver
Dynamic approximation model
Efficient optimization algorithm
Ship type selection subsystem
Advanced parameter setting subsystem
Optimization design subsystem
Post-processing subsystem of optimization results

## Slide 18
This software is applicable to the line optimization and evaluation research of single and multi-hull ship types in inland rivers and coastal areas. It can provide a good platform for the development of new ship types and the research of energy-saving ship types. The software is widely used by ship design and performance research units, and has completed the line optimization research of multiple military and civilian ships, achieving good economic and military benefits.
SBDO-Based Hull Form Optimization

## Slide 19
7500T Bulk Carrier hull form Optimization Design
Optimization Case
 | Initial ship | Optimize ship | Differences
Δ | 9477.19m3 | 9475.11 m3 | -0.02%
XCB | 65.84 m | 64.24 m | -2.42%
WS | 3183.81 m2 | 3163.57 m2 | -0.64%
CB | 0.8654 | 0.8654 | 0.00%
RT | 125.83 KN | 122.14 KN | -2.93%

## Slide 20
Optimized design of 3300m³ LPG
——Optimize ship ——Initial ship
The designed speed is 13 knots, reducing resistance by 2.44% and increasing propulsion efficiency by 4.96%.
Initial ship
Optimization Case
Optimize ship

## Slide 21
A case of installing a bulbous bow on a bulk carrier
Optimization Case

## Slide 22
Optimization Design of the Marine Propeller Pre-Swirl Duct for a Container Ship
Optimization design technology route based on approximate models
Intelligent
Optimization Algorithm
Data
transmission
Objective function
Design variables
Constraint conditions
Intelligent CAD
Performance Evaluation
Approximate model
The energy-saving effect reached 3.59%.
Optimization Case

## Slide 23
Outline
1
Research Background
2
SBDO-Based Hull Form Optimization
3
GeneHull Intelligent Design Platform
4
AI Agents for Autonomous Hull Design
5
Summary and Outlook

## Slide 24
GeneHull Intelligent Design Platform
The main problems existing in ship CAD software
(1)The lack of an autonomous geometric core makes it difficult to achieve parametric geometric modeling for complex ship shapes;
(2) The connection between design and simulation data is not smooth;
(3) The intelligent design capability is weak.
Based on the unified model, achieve design simulation optimization and complete the entire link connection.
Reconstruct the parametric modeling architecture based on the SGK core
Realizing intelligent reasoning of knowledge through large models

## Slide 25
GeneHull Intelligent Design Platform
GeneHull Ship Intelligent Design and Optimization Platform
Based on the SGK core of CSSC SEAGOSOFT, the intelligent design and optimization platform for ships - GeneHull was independently developed. This platform can achieve parametric geometric modeling of complex hulls, embed multiple types of ship performance knowledge bases, and integrate with mainstream CFD simulation software. It supports the "design - simulation - optimization" integrated process and can be applied to the intelligent design and simulation of various ship types, significantly improving the design quality and efficiency of ships.

## Slide 26
Knowledge Base Layer
Inference Layer
CAD Layer
Software system architecture
Key Modules
KBE User Design Interface
Parameter Indicator Input
Ship CAD System
Knowledge Reasoning
Product Solution
Knowledge Rule Database
Engineering Case Database
LLM
Qwen2.5/KIMI/DEEPSEEK, etc.
Knowledge Graph
Knowledge Representation
Knowledge Acquisition
Knowledge Integration
Knowledge Management
Design Case
Expert Experience
Written Documents
Ship Hull Form Intelligent Reasoning System
Parameter Database
Hull Form Knowledge Graph Database
Ship Type Database
Parametric Model Database
Specification Database
Expert Experience Database
Parametric CAD System
Standard query
Design guidance for hull form
Recommended main dimensions and ship type
Scheme specification verification
Offer various initial ship designsProvide parametric models and various parameter-driven deformations
Personalize adjustments to local parameters and constraints
Based on the characteristics of the ship types, the parameter sensitivity of different ship types was analyzed.
Construct a knowledge graph that links various parameters with the performance of the ship body

## Slide 27
Number | Geometric meaning | 参数符号
1 | Starting point coordinates | 
2 |  | 
3 | Termination point coordinates | 
4 |  | 
5 | The corner cut at the starting point | 
6 | The sharp corner at the end point | 
7 | Curvature at the starting point | 
8 | Curvature at the end point | 
9 | The area between the curve and the x-axis | 
10 | Area-type heart | 
11 |  | 
Position parameters mainly refer to the numerical values of the coordinates at the starting and ending points of the curve；
Integral parameters mainly include the area value enclosed by the curve and the coordinate axis, as well as the coordinate values of the center of the curve shape;
Differential parameters mainly refer to the values of the tangent angle and curvature at the starting and ending positions of the curve.
Key Modules
WUT-SPLINE

## Slide 28
Key Modules
Parametric modeling framework based on the WUT-SPLINE

## Slide 29
Construction of the ship form line knowledge base
(1) Collect data on ship line design (such as ship practical design manuals, relevant literature, actual ship data, and line knowledge maps, etc.)
(2) Construction of the ship profile knowledge base
① Mother model instance database
② Design rule database
③ Hull form knowledge graph database
Key Modules

## Slide 30
1.Instance-based reasoning method: By designing a distance between the requirements and the characteristic values of each instance to represent the degree of similarity, similar ship types can be retrieved. The commonly used algorithm is the nearest neighbor search algorithm.
2.Rule-based knowledge reasoning: Determine the validity of the rule premises. If the conditions are met, output the corresponding rule conclusion.
3.Model-based knowledge reasoning: Construct a neural network model that reflects the parameter variation patterns of the knowledge graph.
The reasoning methods of each knowledge base
Hybrid reasoning method
Key Modules

## Slide 31
Outline
1
Research Background
2
SBDO-Based Hull Form Optimization
3
GeneHull Intelligent Design Platform
4
AI Agents for Autonomous Hull Design
5
Summary and Outlook

## Slide 32
AI Agents for Autonomous Hull Design
Large language models (LLMs) demonstrate strong natural language understanding, logical reasoning and task planning capabilities; LLM-centered AI Agents feature task decomposition, tool calling, memory learning and autonomous iteration and are reshaping intelligent workflows in industrial software and engineering design.
Task Understanding & Planning
Automatically parse natural-language design requirements into executable sub-task sequences
Tool Calling
Autonomously call CAD modeling, CFD simulation and optimization tools
Memory & Learning
Accumulate design knowledge and past solutions across iterations
Multi-Agent Collaboration
Specialized agents collaborate to complete complex hull design workflows
Provide a new path for hull design to move from ""computer-aided"" to ""autonomous intelligence""
AI Agents: Toward Autonomous Design

## Slide 33
AI Agents for Autonomous Hull Design
Natural-language design requirements (ship type / dimensions / performance / constraints)
Planning Agent: requirement parsing, task decomposition and scheduling
Parametric Geometry Modeling
GeneHull / SGK geometric kernel
Hull-Form Knowledge Reasoning
Knowledge base + rule base + knowledge graph
Rapid Performance Evaluation
CFD + deep-learning surrogates
Optimization Decision
Intelligent optimization algorithms
Output the optimal hull design and analysis report
Evaluation feedback drives autonomous agent iteration
Building a "humans state requirements, agents design" paradigm: designers focus on requirement definition and key decisions, while AI Agents autonomously perform repetitive tasks such as parametric modeling, knowledge reasoning, performance evaluation and iterative optimization — greatly improving design efficiency and quality.
AI-Agent Architecture on GeneHull

## Slide 34
AI Agents for Autonomous Hull Design
① Domain knowledge alignment: general LLMs lack ship-design expertise and must be deeply integrated with domain knowledge;
② Tool encapsulation & orchestration: CAD/CFD software interfaces are complex and must be standardized into agent-usable tools;
③ Geometry & knowledge representation: hull geometry and design knowledge need structured, computable representations;
④ Reliability verification: agent-generated designs require CFD/experimental validation and expert review.
Implementation Path
① Take the SGK geometric kernel and GeneHull platform as the foundation, encapsulating the modeling–deformation–evaluation–optimization toolchain;
② Take the hull knowledge base, design rule base and knowledge graph as the agent's domain knowledge sources;
③ Take the deep-learning surrogate models (graph neural networks, symbolic regression) for rapid hydrodynamic evaluation;
④ Establish a ""agent-autonomous design + expert review"" human-machine collaborative loop.
The team already has complete technical foundations in geometric kernels, intelligent design platforms, knowledge bases and surrogate models, laying a solid foundation for AI-Agent autonomous hull design
Key Challenges and Implementation Path
Key Challenges

## Slide 35
From Lines Plan to an Editable .ahp Project
Case Overview
1
1
Original input: lines plan
Raw geometric input required for modeling
2
Final output: editable project
Hull surface and project, editable after import into GeneHull
Longitudinal lines
12
WUT segments
105
Straight segments
67
Shape control curves
10
AHP project objects
214

## Slide 36
Six-Step Modeling Chain: from Lines Plan to Editable Project
Modeling workflow
2
01
AI
AI line recognition
Centerline profile, flat bottom line, flat side line, design waterline, deck side line (h, w), forecastle deck side line (h, w), bulwark top line (h, w)
02
AI
Longitudinal lines & WUT
Split each line into segments at its intersections with adjacent stations; endpoint coordinates come from the table of offsets, fullness and tangent angles from the lines plan.
03
AI
Shape control curves
Read from the body plan, station by station, the fullness of each segment and the tangent angles to the longitudinal lines; fit them along the length with WUT splines into fullness and tangent-angle curves.
04
Human
Sections & section groups
Divide the hull into regions by its features and assign a section to each; sections bind to the longitudinal lines so the section group varies smoothly along the ship.
05
Human
Hull skinning
Loft the section groups into hull surfaces.
06
AI
Stern fin construction
First create the fin outline curves to control the circumferential shape; then connect proportional points on the outlines into guide curves controlling the axial shape.
Human-AI division of labor in the AHP project
Human: section curves, section groups, hull skinning, and hull region division; all other steps are completed interactively with AI.

## Slide 37
Step 1 | AI Recognition of Longitudinal Feature Lines
Step 1 · AI line recognition
3
AI recognition workflow
1
Locate the drawing and target lines
A 2D feature line needs one curve only (e.g., the flat bottom line, read from the half-breadth plan); a 3D line needs two curves for width and height (e.g., the deck side line).
2
Locate intersections with station lines
A station line gives the X coordinate; the table of offsets supplies Y and Z (breadth and height), so the intersection is fixed.
3
Read end tangent angles
Draw tangents at both endpoints and measure the tangent angles.
4
Compute the segment fullness
Form the rectangle whose diagonal joins the endpoints (area S); the integral area between curve and edge is A, so fullness F = A/S.
Locate regions and identify target lines
Tangent angles near intersections
Area and control-value checks

## Slide 38
Step 2 | WUT Parameters and Five Elements
Step 2 · Longitudinal lines and WUT fitting
4
WUT parameters in GeneHull
• The panel shows endpoints, tangent angles, fullness, and sample count
• AI drafts initial parameters from recognition, then verifies by curve read-back
Five elements
1
Start point P0
Start endpoint of the segment
2
End point P1
End endpoint of the segment
3
Two tangent angles
Control entry and exit tangents
4
Fullness F
Area ratio F = A/S controls the bend
WUT for curved / transition segments, straight lines for flat runs

## Slide 39
Step 2 | Extracted Longitudinal Feature Lines
Step 2 · Longitudinal lines and WUT fitting
5
Longitudinal feature lines — top view
Read-back of all 12 longitudinal feature lines (top view)
Longitudinal feature lines — side view
Read-back of all 12 longitudinal feature lines (side view)

## Slide 40
Step 2 | Verification of Fitting Parameters
Step 2 · Longitudinal lines and WUT fitting
6
Longitudinal lines
12
WUT segments
105
Straight segments
67
Geometric checks
✓ Fitted endpoints coincide with extracted endpoints
✓ Adjacent segments share nodes with tangent continuity
✓ WUT fullness within valid fitting range
✓ Flat runs kept as straight lines, no spurious bending
Consistency checks
• Segment count, endpoints, and point counts agree
• End tangent angles match adjacent segments
• Fullness consistent with segment shape
• 65 parameter rows traceable to their segments
Once verified, the longitudinal feature lines serve as upstream curves for the section templates.

## Slide 41
Step 3 | Tangent-Angle and Fullness Curves
Step 3 · Shape control curves
7
Overview of shape control curves in GeneHull
Each family is fitted segment by segment along the length and sampled at target stations
Two families: 4 fullness curves + 6 tangent-angle curve groups
Fullness example: FULL1 bilge fullness, straight at midship
Parameters vary along the length with key station readings retained
Tangent-angle example: bottom angle section tangent angle at the flat bottom, along the length

## Slide 42
Step 3 | WUT Fitting of Shape Control Curves
Step 3 · Shape control curves
8
Fullness example: FULL2 section curve between waterline and deck line
Tangent-angle example: bottom angle section tangent angle at the flat bottom, along the length
Four steps of WUT fitting
1
Segment by shape
Flat and transition runs along the length
2
Fix endpoints
Adjacent segments share nodes
3
Encode control values
z-values encode angle or fullness
4
Write into sections
Sampled at stations, sent to matching segment
Shape control curves are segmented independently along the length

## Slide 43
Step 3 | Verification of Shape Control Parameters
Step 3 · Shape control curves
9
Tangent-angle check: BOT bottom angle (always 0 in parallel midbody)
Tangent-angle checks
• End transitions consistent with the horizontal datum
• Angle changes between adjacent stations remain continuous
• Abnormal reversals and bad intersections investigated individually
Fullness check: FULL4 (bulwark segment, constant straight-chord 0.500)
Fullness checks
• Values map reliably to the corresponding WUT segments
• 0.500 means the segment degenerates to a straight chord
• Key curve values agree with 3D read-back

## Slide 44
Step 4 | Building the Single-Station Section Template
Step 4 · Section templates and section groups
10
Section segment binding in GeneHull
The panel shows, segment by segment, how key points bind to the upstream longitudinal curves; each segment needs its matching section template.
Four steps of section construction
1
Choose position
Any x position within the segment range
2
Bind endpoint coordinates
Endpoint coordinates bind to the longitudinal lines
3
Bind fullness & angles
Intersection angles and segment fullness bind to the lines
4
Check continuity
Shared nodes with verified tangents
Proceed to the section group after continuity passes

## Slide 45
Step 4 | From Single Template to the Full Section Group
Step 4 · Section templates and section groups
11
Single-station template
• Template fixes segment composition and endpoint curves
• Sections placed evenly within each segment
Full-ship sections
145
Generated evenly with per-segment counts
Generation logic
• Template inherits the upstream curves
• Generated evenly within each segment range
• Grouped by segment-composition changes
Full-ship section group
Sections placed evenly within each segment

## Slide 46
Step 4 | Hull Region Arrangement
Step 4 · Section templates and section groups
12
Isomorphic grouping and hull regions
Group | Length range / m | Stations | Segments | Segment composition
Midship-aft body | −2.99 – 165.0 | 40 | 4 | Flat bottom → bilge curve → flat side → deck
Fwd body 1 | 165.0 – 167.467 | 20 | 5 | Flat bottom → bilge curve → above-water curve → flat side → deck
Fwd body 2 | 167.467 – 177.318 | 20 | 4 | Flat bottom → bilge curve → above-water curve → deck
Fwd body 3 | 177.318 – 182.874 | 20 | 5 | Flat bottom → bilge curve → above-water curve → deck → forecastle transition arc
Fwd body 4 | 182.874 – 183.070 | 5 | 6 | Flat bottom → bilge curve → above-water curve → deck → forecastle → bulwark transition arc
Fwd body 5 | 183.070 – 197.000 | 40 | 6 | Flat bottom → bilge curve → above-water curve → deck → forecastle → bulwark

## Slide 47
Step 5 | Hull Skinning from Section Groups
Step 5 · Hull skinning
13
Hull skinning section groups build a continuous surface; main hull completed
Input
• 6 section groups
• 145 sections sampled along the length
Skinned surfaces
6
Main hull completed
Generation rules
• Consistent segment count, endpoints, and point count
• Adjacent sections connected in station order
• Group boundaries kept as separate surfaces

## Slide 48
Step 6 | AI Recognition of Fin Outlines and Guide Curves
Step 6 · Stern fin and project output
14
Fin surface and root connection region
6 outline curves and 12 guide curves
• Outlines define the root edge, end face, and side boundaries; guide curves control the mapping of the 6 control points on the surface.
• After outline reshaping, the equal-t control points update with the outlines and rejoin the main hull surface.

## Slide 49
Step 6 | B-Spline Control and Guide Curve Construction
Step 6 · Stern fin and project output
15
B-splines and guide curves
Fin injection check: outlines, guide curves, and main hull root edge
1
Outline curves 1-4
B-spline control-point curves controlling the circumferential shape
2
Outline curve 5
Controls the shaft outlet shape and position
3
Outline curve 6
Obtained by offsetting outline curve 5
4
12 guide curves
Fitted through proportional points on the 6 outlines controlling the fin radial shape

## Slide 50
Step 6 | Fin Integration and Geometric Verification
Step 6 · Stern fin and project output
16
Fin root fitting, local blending, and continuous connection to the main hull
Project objects
214
Dependency edges
230
Final project output
• Editable GeneHull .ahp project
• Nodes, expressions, and dependencies retained
Integration checks
✓ Root edge fits the main hull surface
✓ Cutout boundary follows the curves
✓ Fin joins the hull continuously
✓ Nodes, dependencies, and scripts readable

## Slide 51
Outline
1
Research Background
2
SBDO-Based Hull Form Optimization
3
GeneHull Intelligent Design Platform
4
AI Agents for Autonomous Hull Design
5
Summary and Outlook

## Slide 52
Summary and Outlook
Summary of Main Work
SBDO hull form optimization: RBF / FFD deformation modules and CFD-based optimization software, validated on multiple full-scale ship projects.
GeneHull intelligent design platform: parametric modeling on the SGK kernel + knowledge bases + CBR/RBR/MBR reasoning; concept design within 5 minutes.
AI performance prediction: graph neural networks and symbolic regression enable fast, generalizable resistance and flow-field prediction.
Future Outlook
Parametric modeling software with independent IP (SGK kernel) embedded with LLMs
Mine implicit knowledge from existing hull forms; expand the knowledge base to more ship types and performances
LLM-based intelligent reasoning and agent-based rapid prototype generation for ship concept design
Deeply integrate generative AI, multimodal data and intelligent optimization with domain knowledge and rules
Ultimate goal: an intelligent ship design theory, methodology and prototype system fusing physical laws · domain knowledge · data intelligence · computable geometry, leading to AI-Agent autonomous hull design
Main Work and Future Directions

## Slide 53
Summary and Outlook
1. Develop ship parametric geometric modeling software with fully independent IP (based on the SGK kernel), embedding a large model (e.g. Qwen2.5 or others);
2. Mine implicit design knowledge from existing hull forms and expand the knowledge base (covering more ship types and performances);
3. Develop LLM-based intelligent reasoning methods, achieving agent-based rapid prototype generation to support ship concept design;
4. Deeply integrate generative AI, multimodal data processing and intelligent optimization algorithms with hull-design domain knowledge, expert experience, classification-society rules and maritime regulations, ultimately building a ship intelligent-design theory, methodology and prototype system that fuses physical laws, domain knowledge, data intelligence and computable geometry.

## Slide 54
Thank You.